HOW TO COLLECT AND VIEW DATA USING PYBAR (DRAFT 3)
Dennis Feng

Actions: Click (single-click), D-click (double click), Type (type, then press enter)

SETUP THE PROGRAMS (GET THEM ON-SCREEN)

1. Terminal
  1. Click the terminal icon (little black rectangle) on the upper menu bar of the entire screen. This opens up the terminal window.
  2. Type in "cd /home/pixel/pybar/pybar_github/pybar/homemade_scripts". This changes your directory to the homemade_scripts folder, which you need to be at in order to run the scripts. Check by seeing that the most recent line in the terminal says something like “[pixel@_____________ homemade_scripts]$”, noticing the “homemade_scripts” part.
2. File Browser
  1. Click the File Browser icon (little file cabinet) on the upper menu bar of the entire screen. This opens up the File Browser.
  2. In the "Location:" text box, type in "/home/pixel/pybar/pybar_github/pybar/module_1"; this changes the current directory of the File Browser to be the module_1 folder.
  3. Click File, then New Tab, to create a new tab. In the "Location:" box of the new tab, type in "/home/pixel/pybar/pybar_github/pybar/homemade_scripts".
Now you have two tabs, one for module_1, and one for homemade_scripts, that you can easily	access by clicking on the tab headers.

1. Sublime Text
  1. D-click the following files in the File Browser. This opens them up in Sublime Text automatically, so you don't have to worry about opening up the Sublime Text program itself. Note that there may be a pop up that asks you to update Sublime Text: whenever that pops up, simply cancel it.
  2. *Optional: For more convenience later, you may want to shift the tabs to be in a certain logical order so you can access them more easily. I like to put them in the following order.
run_extra_info.txt - self-recording info
aggregate_data_info.txt - self-recording info
automate_scans.sh
scan_ext_trigger_stop_mode.py
convert_h5_to_Hits.py - converting file
convert_Hits_to_EventsCR.cpp - converting file
aggregate_Hits_and_EventsCR.cpp - converting file
view_individual_events.cpp - viewing data
view_all_events.cpp - viewing data

GENERAL PROCEDURE TO GATHER AND VIEW DATA

1. Turn all the hardware on
  1. Use HV power supply to turn on the field cage and the GEMs.
  2. Make sure everything is plugged in into the USBPix module.
  3. Turn on both power supplies for the USBPix module and the FE-I4 chip.

Note that when working with the scripts, you can look for the “@@@@@@@@@@@” lines to help indicate where you can change the code. You can use the Find utility by clicking the "Find" tab, and then clicking "Find...". This opens up a little panel at the bottom of the window, in which you could type "@@@@@@@@@@@@", and the Find utility will take you to the correct line.

1. Gather data from pybar (_interpreted.h5 files)
  1. In Sublime Text, click the “automate_scans.sh” tab. Near the top of the file, you can change NUM_SCANS to the number of repetitions of SM (stop mode) scans you want. I generally suggest around 20 if you want to do a batch job.
  2. In Sublime Text, click the “scan_ext_trigger_stop_mode.py” tab. You can change the number of events per scan by changing the “max_triggers” variable to whatever number you want. I generally suggest 10 to 50.
  3. Type "bash automate_scans.sh" in the terminal to start the scans. The h5 data files and pdf files will automatically be sent to the module_1 folder.
  4. In the File Browser, look in module_1 and look for the most recent scan. Remember the h5 file number for it to use in the next step.
  5. In Sublime Text, click the “run_extra_info.txt” tab, and record the info about the scans you are running. Each line starts with the h5 file num, which you should have from the previous step.

1. Convert the _interpreted.h5 files into Hits and EventsCR files. They need to be converted in order to use the data analysis scripts.
  1. In Sublime Text, click the “convert_h5_to_Hits.py” tab. This script creates a Hits file (contains info for each hit) corresponding to each h5 file chosen. Scroll down to the "main" method (it starts with if __name__ == "__main__":) and change “h5_file_nums” variable to be the list of h5 files you want to convert.
  2. In Sublime Text, click the “convert_Hits_to_EventsCR.cpp” tab. This script creates an EventsCR file (contains info for each event) corresponding to each h5 file chosen. Change “fileNums[numFiles]” variable to be the list of h5 files you chose and “numFiles” variable to be the number of those files.
  3. Type "python convert_h5_to_Hits.py" into the terminal to run the script for converting to Hits files.
  4. Type "root -l -x convert_Hits_to_EventsCR.cpp" into the terminal to run the script for converting to EventsCR files. Ignore the errors and warnings; they simply tell you whenever a line fit fails, but they don't break the process. Then type ".q" to quit ROOT and return to normal terminal use.

Now you should have the Hits and EventsCR files in your module_1 folder, which you can run	data analysis on.

View histograms on the data
  1. In Sublime Text, click the “view_individual_events.cpp” tab.
  2. Change the “file_num_input” variable to be the h5 file num that you want to view.
  3. Check to make sure the view_option is "1".
  4. Type in "root -l -x view_individual_events.cpp" in the terminal to run the script.
    1. Press enter to advance to next event, b to go to previous event, or q to quit.